## Slide 1
Water and Draft Systems
Steam School Notes | Water and Draft Systems Overview
Two continuous processes manage steam production
• Water management: feedwater enters through injectors or pumps • Draft management: hot gases exit through smokebox and stack • Both systems work together from pressurization to exhaust
• Exhaust steam powers engine and drives draft system • Spent steam from pump and injectors preheats feedwater • Sediment removed via blowdown valve for safety and efficiency
Water and draft systems form one integrated cycle enabling steady steam production under varying loads

## Slide 2
Direct-Drive Feedwater Pump
Steam School Notes | Feedwater Systems
Reciprocating plunger pump with gear reduction
• Small crankshaft gear drives larger pump gear; offset crankpin converts rotation to reciprocating motion • Inlet and outlet check valves control water flow • Bypass valve enables feed-rate control; relief valve prevents over-pressurization
Advantages • Simple, durable, and mechanically efficient • No steam consumption • Output increases naturally with engine workload • Very reliable at road speed

## Slide 3
Direct-Drive Feedwater Pump
Steam School Notes | Feedwater Systems
Reciprocating plunger pump with gear reduction
Disadvantages • Cannot pump when engine is stopped • Weak delivery at very low engine speeds • Requires tight packing and good check-valve condition • Feed rate fixed by gear ratio and engine RPM, limiting fine control • Pump always engaged with engine

## Slide 4
Marsh Pump
Steam School Notes | Feedwater Systems
Independent steam-driven feedwater pump
• Self-contained steam engine dedicated to water movement • Simplex design: one steam cylinder and one water cylinder on common piston rod • Internal piston-valve mechanism automatically shifts steam admission for continuous reciprocation
• Operates independently of engine speed • Exhausts spent steam directly into incoming feedwater • Preheating reduces thermal shock to boiler flues • Improves overall steaming efficiency
Marsh pump provides independent feedwater delivery and preheating in one integrated unit

## Slide 5
Feedwater Heater
Steam School Notes | Feedwater Systems
Non-pressurized heater warms incoming water
• Small chamber with bank of small tubes carrying exhaust steam • Surrounding water space absorbs heat from exhaust • Water space supplied and pressurized by mechanical pump • Check valve at pump discharge prevents boiler pressure backflow
• Reduces thermal shock to boiler flues • Improves steaming efficiency • Case shipped all engines with heater • Heater inactive on engines without pump (becomes passive heat reservoir)

## Slide 6
Smokebox
Steam School Notes | Exhaust and Draft System
Central meeting point of entire draft system
• Front compartment of boiler located behind stack • Collects hot gases from boiler flues and combines them with engine exhaust steam • Exhaust pulse through nozzle creates vacuum pulling fire's hot gases through flues and up stack
Components and Maintenance • Contains exhaust nozzle, petticoat pipe, blower ring, flue ends • Must remain reasonably tight to prevent draft loss • Leaky smokebox weakens draft and reduces engine steaming • Regular cleaning essential: soot buildup chokes flues and impairs draft • Case engines typically feature hinged or bolted door for maintenance

## Slide 7
Stack
Steam School Notes | Exhaust and Draft System
Upper end of draft system creates partial vacuum
• Vertical path for exhaust steam, smoke, ash, and cinders • Works in partnership with exhaust nozzle in smokebox • Exhaust steam jet upward creates partial vacuum pulling hot gases through flues
• Engine breathes harder under load: more exhaust pulses mean stronger draft • Height keeps sparks away from operator • Reduces risk of fire to dry stubble or straw around machine • More frequent and forceful exhaust pulses create stronger draft
Stack height and exhaust velocity form core of locomotive-type draft system

## Slide 8
Spark Arresters
Steam School Notes | Exhaust and Draft System
Devices prevent live cinders escaping stack
Arrester Types • Screen arresters: fine wire mesh catches sparks before exit • Deflector-cone arresters: force exhaust to change direction, heavy cinders fall out • Cyclone or centrifugal arresters: spin exhaust gases, fling embers into chamber • Stack caps: incorporate baffles or screens reducing spark throw
Design Balance • Must stop sparks without choking draft • Too fine a screen smothers fire and ruins steaming • Too open a design risks field fire • Many engines had removable or seasonal arresters for seasonal conditions
Too restrictive an arrester can smother the fire and ruin steaming

## Slide 9
Blower
Steam School Notes | Exhaust and Draft System
Steam-driven nozzles create draft when engine slows
• Ring or series of small nozzles inside base of stack • When blower valve opens, live steam shoots upward into stack • Steam jet creates vacuum in smokebox, pulling hot gases through flues
Uses • Starting fire to get draft before engine can run • Maintaining draft while stopped or idling • Controlling fire: quick burst brightens fire or clears smoke • Safety: prevents fire from backing up into flues during coasting
Blower uses live steam and must be used sparingly to avoid wasting steam and overfiring boiler

## Slide 10
Exhaust Nozzle
Steam School Notes | Exhaust and Draft System
Precisely sized opening creates draft through velocity
• Small opening at base of stack where spent steam discharges into smokebox • Every exhaust pulse forces steam through nozzle at high velocity • Jet shoots upward into stack creating partial vacuum in smokebox
• Vacuum pulls hot gases through flues and fresh air up through grates and firebed • More frequent and forceful exhaust pulses create stronger draft • Engine fires up under load due to increased exhaust frequency and force • Diameter and position are critical to performance • Too small nozzle chokes exhaust and wastes power • Too large nozzle weakens draft making engine sluggish to steam
Exhaust nozzle provides core draft function through precise sizing for each boiler-cylinder combination

## Slide 11
Blower and Nozzle Integration
Steam School Notes | Exhaust and Draft System
Exhaust nozzle and blower work together
• Nozzle works hand-in-hand with stack, smokebox, and blower • When engine running: nozzle provides nearly all draft • When engine stopped or drifting: blower takes over to keep fire from backing up

## Slide 12
Blowdown Valve
Steam School Notes | Blowdown System
Bottom-mounted valve removes accumulated sediment
• Mounted at very bottom of boiler on mud ring • Removes heaviest sediment settling out of water during operation • When opened, boiler pressure forces water and sediment out in fast, powerful jet
Function and Maintenance • Minerals, rust flakes, and impurities collect in lowest part of shell • Accumulated material insulates metal from water, causes uneven heating, contributes to scale • Rapid discharge scours mud ring and carries solids out of boiler • Normally done briefly and regularly (once or twice daily) rather than long intervals • Prevents sediment buildup and maintains boiler efficiency
Operators must stand clear of discharge; hot water and steam plume is dangerous

## Slide 13
Blowdown Valve Design
Steam School Notes | Blowdown System
Strong, reliable valve withstands full boiler pressure
• Must be absolutely tight when closed • Typically self-cleaning Y-valve designed for full boiler pressure • Straight-through quick-opening valves also used • Integral part of routine maintenance alongside proper water treatment and washouts
Blowdown valve keeps boiler clean, efficient, and safe through regular sediment removal