## Slide 1
Dome to Exhaust
Steam School Notes | 7 Dome to Exhaust
Steam path from boiler to exhaust
• Dome valve: main shutoff on dome • Throttle: operator control valve • Governor: automatic speed regulator • Steam chest: distribution chamber • Motor: engine assembly • Cylinder drains: water release valves • Exhaust: spent steam discharge

## Slide 2
The Dome
Steam School Notes | 7 Dome to Exhaust
Dome collects dry steam above waterline
• Raised chamber mounted on boiler shell • Provides space for driest steam collection • Gravity and distance separate water from steam • Ensures relatively dry steam reaches throttle
• Built from heavy plate, riveted or welded integral to shell • Must withstand full boiler pressure • Subject to same inspection as boiler • Mounts safety valve, steam gauge line, and fittings • Height and volume carefully balanced for steam quality and boiler strength
Dome is boiler steam reservoir ensuring dry steam supply

## Slide 3
Dome Valve
Steam School Notes | 7 Dome to Exhaust
Main shutoff controlling boiler to engine steam
• Located on boiler dome • Controls steam flow to engine steam line • Fully open during operation, fully closed for maintenance • Stop valve, not regulating valve • Must be absolutely tight when closed • Seats on dome where driest steam collects
• Must be opened slowly to avoid thermal shock • Opening is first step in motor warm-up • Closing while engine works would starve steam chest and damage valve gear
Leaking dome valve allows unexpected steam to throttle. Inspectors pay close attention to condition, packing, and seating.

## Slide 4
Throttle
Steam School Notes | 7 Dome to Exhaust
Operator control metering steam to engine
• Primary operator control over engine • Balanced poppet or slide-type valve • Mounted between dome valve and steam chest • Controlled by lever on platform • Receives only dry steam from dome
• Open smoothly for engine start without violent lurch • Hold intermediate position for precise steam metering • Close tightly to prevent creeping when shut
Worn or leaking throttle can allow steam to engine when closed, causing unexpected creeping or turning. Test throttle tightness before belting and during inspections.
Throttle is power valve giving operator direct fine-grained steam control

## Slide 5
Governor
Steam School Notes | 7 Dome to Exhaust
Automatic speed regulator maintaining steady RPM
• Automatic speed-regulating device • Keeps traction engine at steady RPM regardless of load • Mounted on crankshaft or belt-driven • Provides continuous hands-off adjustment
• Engine speeds up: flyballs move outward under centrifugal force • Collar lifts, linkage partially closes throttle • Engine slows down: balls fall inward, collar drops • Linkage opens throttle wider, self-correcting system
Worn or sticky governor causes hunting, sluggish response, or dangerous overspeed. Keep governors clean, lubricated, and inspected regularly.
Governor automatically balances steam supply against load for smooth safe operation

## Slide 6
Steam Chest
Steam School Notes | 7 Dome to Exhaust
Chamber distributing steam to cylinder
• Chamber alongside or above cylinder • Buffer and control space between throttle and cylinder • Receives steam at operator-selected pressure • Valve gear admits steam alternately to each end
• Contains slide valve or piston valve moving with crankshaft • Valve uncovers and covers ports leading to cylinder • Working pressure lower than boiler pressure • Governor opens throttle wider under heavy load, raising pressure • Governor closes throttle under light load, reducing pressure
Leaks past valve waste steam, reduce power, cause engine creep when throttle closed. Critical inspection point.
Steam chest is control chamber metering steam delivery to cylinder

## Slide 7
Motor
Steam School Notes | 7 Dome to Exhaust
Engine assembly converting pressure to mechanical work
• Complete steam-engine assembly on traction engine • Includes cylinder, piston, crosshead, connecting rod, crankshaft, valve gear, steam chest • Converts boiler pressure into mechanical work • Turns reciprocating motion into rotary motion
• Steam admitted through valve gear pushes piston • Motion drives flywheel, gearing, and rear wheels • Throttle, governor, steam chest, and cylinder drains interact directly • Form control system determining motor steam reception and exhaust

## Slide 8
Cylinder Drains
Steam School Notes | 7 Dome to Exhaust
Water removal valves preventing hydraulic damage
• Small valves at lowest points of cylinder ends • Remove water before it can cause damage • Water incompressible; compression causes head gasket, piston, or head damage • Also called cylinder cocks
• Operator opens drains before engine starts • Water blown out by steam pressure as engine begins to move • Produces jets of water and white steam from cylinder ends • Close drains once cylinder warms and drains run clear • Allows engine to develop full power
Stuck-closed drain risks catastrophic damage. Leaking drain wastes steam and reduces power. Test drains before moving engine and keep clean and lubricated.

## Slide 9
Cylinder Drains
Steam School Notes | 7 Dome to Exhaust
Water removal valves preventing hydraulic damage
• Must be easy to operate, reliable, and tight when closed • Serve second purpose: prevent vacuum lock with throttle closed • Opening drains allows air to enter or steam to escape freely • Prevents piston being pulled hard against cylinder end
Cylinder drains are engine safety valves protecting motor from hydraulic damage

## Slide 10
Steam-Chest Drain
Steam School Notes | 7 Dome to Exhaust
Condensate removal from steam chest during warm-up
• Small valve at bottom of steam chest • Removes condensate forming when engine cold or sitting • Steam chest first space receiving steam when throttle opened • Accumulates water quickly during warm-up
• Opened together with cylinder drains during startup • Allows water to escape before reaching cylinder • Steam-chest drain closed first once it blows clear • Cylinder drains closed after cylinders themselves hot and dry
Steam-chest drain prevents water slugs entering valve passages and cylinder

## Slide 11
Exhaust
Steam School Notes | 7 Dome to Exhaust
Spent steam discharge from cylinder
• Spent steam released from cylinder after work on piston • Escapes into exhaust passage when valve gear uncovers exhaust port • Directed into smokebox through exhaust nozzle as high-velocity jet
• Clears cylinder so fresh steam can enter on next stroke • Powers draft, creating vacuum in smokebox • Vacuum pulls air through fire and flues
Exhaust both ends engine power cycle and begins boiler combustion cycle