## Slide 1
Power Path Overview
Steam School Notes | 8 Crankdisk to Traction
Piston force to traction motion
• Crankdisk converts piston motion to rotary motion • Pulley wheel provides belt-drive power output • Clutch connects/disconnects engine from traction gearing • Gearing reduces speed and multiplies torque • Differential permits different wheel speeds • Rear wheels convert rotary motion to traction
Drive train converts cylinder force into controlled, powerful motion at the wheels

## Slide 2
Crankdisk Function
Steam School Notes | 8 Crankdisk to Traction
Crankdisk converts reciprocating motion to rotation
• Large circular plate mounted on main shaft • Crankpin set off-center; connecting rod attaches here • Drives flywheel, pulley wheel, and traction gearing • Acts as counterweight to balance piston and rod • Reduces vibration and smooths engine operation
Design Advantages • Simple and strong construction • Easy to manufacture • Broad, rigid structure for mounting crankpin • Large mass contributes rotational inertia • Helps engine carry through dead centers
Crankdisk is the mechanical heart converting piston motion into rotary output

## Slide 3
Twin-Cylinder Arrangement
Steam School Notes | 8 Crankdisk to Traction
Twin cylinders use multi-throw crankshaft design
• Single-cylinder: one crankdisk on main shaft • Twin-cylinder: crankshaft with two crank throws • Each cylinder has its own crankpin • Throws set at angle (often 90 degrees) • Ensures smooth torque and eliminates dead centers
Twin-Cylinder Benefits • Engine starts from any position • Provides more uniform power delivery • Crankshaft is multi-throw forging or built-up assembly

## Slide 4
Pulley Wheel Power Output
Steam School Notes | 8 Crankdisk to Traction
Pulley provides belt-drive for stationary work
• Mounted on crankshaft, turns at full engine speed • Wide flat cast-iron wheel with smooth rim • Grips heavy canvas or leather belt • Powers threshers, sawmills, feed grinders, pumps • Governor maintains constant RPM • Delivers smooth continuous rotary power
Operating Characteristics • Ideal for machinery running at several hundred RPM • Diameter chosen to match common farm equipment • Optional pulley sizes available for different applications • Contributes to crankshaft balance • Freewheels when not in use
Pulley wheel transforms traction engine into portable stationary power plant

## Slide 5
Clutch Purpose and Design
Steam School Notes | 8 Crankdisk to Traction
Clutch connects or disconnects traction gearing
• Sliding-hub friction clutch built on crankshaft • Not required for starting from rest • Allows engine to run without moving wheels • Enables backing into a belt • Used for idling and gearing adjustments
Components • Hub slides on crankshaft via keyway • Guided by lever arrangement on operator platform • Fork fits into grooves machined around hub • Pulling lever moves fork and slides hub axially
Clutch gives operator control over power delivery to gearing and pulley

## Slide 6
Clutch Expanding-Shoe Mechanism
Steam School Notes | 8 Crankdisk to Traction
Spokes and shoes expand outward to grip
Disengaged Position • Spokes sit at angle, pulling shoes inward • Shoe circumference smaller than pulley inside • Pulley spins freely around crankshaft
Engaged Position • Fork pushes hub forward • Spokes straighten and force shoes outward • Shoe circle expands to grip pulley inside • Creates strong positive friction fit

## Slide 7
Clutch Over-Center Locking
Steam School Notes | 8 Crankdisk to Traction
Over-center action locks shoes in engagement
• Spokes pushed past straight-line position • Geometry locks shoes outward • Prevents clutch slipping under load • Operator feels distinct snap or detent • Clutch lever goes over center

## Slide 8
Clutch Retention Methods
Steam School Notes | 8 Crankdisk to Traction
Mechanical methods prevent clutch disengagement
• Ratchet and pawl on clutch lever quadrant • Pawl drops into tooth and holds position • Locking pin or latch dropped into place after engaging • Over-center geometry alone with careful adjustment • Different manufacturers used different systems

## Slide 9
When Clutch Is Actually Needed
Steam School Notes | 8 Crankdisk to Traction
Clutch required only in specific operating modes
• Running belt pulley while keeping engine stationary • Backing into a belt with turning pulley • Stopping machine without stopping engine • Idling engine during gearing adjustments
Normal Operation • In forward operation, clutch engaged and left there • Enormous low-speed torque eliminates need for slip • Engine happily starts from rest with clutch fully engaged
Traction engines produce such high low-speed torque that clutch slip is not needed for normal starts

## Slide 10
Backing Into a Belt
Steam School Notes | 8 Crankdisk to Traction
Clutch must engage to turn pulley wheel backward
• Clutch engaged so wheels turn engine backward • As engine rolls backward, pulley wheel turns • Belt looped over pulley initially slips freely • Increasing tension creates friction on rim • Belt begins turning with pulley • Belt fully stretched, friction established • Belt and pulley rotate together
• Only normal operation scenario requiring rotating engine clutch • Forward work can start from rest with clutch fully engaged • Clutch required because wheels must turn engine backward
Backing into belt is unique case where rotating engine must be clutched to pulley

## Slide 11
First-Motion Pinion
Steam School Notes | 8 Crankdisk to Traction
Pinion transmits crankshaft rotation into gear train
• Small gear mounted directly on crankshaft • First point of contact with traction gearing • Turns at full engine speed • Must be small, strong, precisely fitted • Meshes with intermediate gear directly • On parallel-shaft arrangement (most traction engines)
• Begins necessary speed reduction to drive train • No direction change; shafts parallel • Few unusual machines (road rollers, Shay locomotive) depart from parallel arrangement

## Slide 12
Intermediate Gear Function
Steam School Notes | 8 Crankdisk to Traction
Intermediate gear provides speed reduction and torque transfer
Primary Functions • Speed reduction from first-motion pinion • Passes engine torque to differential on cross shaft • Significantly larger than first-motion pinion • Reduces engine RPM to slow, powerful rotation
Construction and Features • Mounted on short shaft with bearings • Supported by heavy bracket cast into frame • On some engines, slides out of mesh for neutral • Neutral independent from clutch operation • Simple rotation passing along line of parallel gears

## Slide 13
Differential Design Basics
Steam School Notes | 8 Crankdisk to Traction
Differential permits different wheel rotation speeds
Common Type • Flat sun-and-planet differential arrangement • Crown gear cast into platter forming rotating carrier • Pinion gear turns with ring gear • Pinion rotates differential platter • Planet gears mounted on pins
Differential Components • Pinion gear: turns with ring gear • Planet gears: run between crown gear and sun gear • Crown gear: cast into platter face • Sun gear: splined to cross shaft

## Slide 14
Differential Operating Mechanism
Steam School Notes | 8 Crankdisk to Traction
Differential mechanism drives sun gear rotation
Power Flow • Intermediate gear drives ring gear • Ring gear fixed to platter • Platter carries crown gear cast into face • Planet gears run between crown and sun gear • As platter rotates, carries planet gears around • Planet gears drive sun gear on cross shaft
Same-Speed Operation • Both wheels turning same speed • Planet gears orbit without spinning on pins • No speed differential

## Slide 15
Differential Action in Turning
Steam School Notes | 8 Crankdisk to Traction
Planet gears spin to allow wheel speed differences
• Wheels need different speeds in corners • Planet gears rotate on pins • Sun gear turns faster or slower than platter • Each wheel rotates at speed it needs • Outer wheel turns faster than inner
Design Advantages • Compact and flat between frame rails • Extremely rugged and dirt-tolerant • Tolerates misalignment • Handles high torque at low speed • Integrates cleanly with cross shaft and final-drive pinions

## Slide 16
Differential Lock Feature
Steam School Notes | 8 Crankdisk to Traction
Lock ties sun gears for heavy pulling conditions
• Collar slides to tie both sun gears together • Used for plowing or heavy pulling • Prevents wheel slip on difficult soil • Both wheels rotate at same speed • Maximizes traction under extreme loads

## Slide 17
Final-Drive Pinions
Steam School Notes | 8 Crankdisk to Traction
Pinions deliver differential output to bull gears
• One on each end of cross shaft • Small hardened gears of equal size • Keyed or splined to cross shaft • Rotate with cross shaft • Mesh directly with bull gears on rear wheels
Performance Characteristics • Provides largest single speed reduction in drive system • Allows slow, steady, powerful motion • Must be precisely aligned and well-lubricated • Extremely robust to carry full engine torque • After all previous gear reductions
Final-drive pinions create largest speed reduction enabling controlled powerful motion

## Slide 18
Bull Gears Large-Gear Multiplication
Steam School Notes | 8 Crankdisk to Traction
Bull gears multiply torque while reducing speed
Characteristics • Large, heavy gears bolted to rear wheel hubs • Often largest gears on entire machine • Several feet in diameter • Final mechanical link between engine and ground • Multiply torque dramatically
Construction and Mounting • Cast iron or steel • Bolted to wheel hub or wheel spokes • Open to air; not enclosed • Require regular lubrication • Wide deep teeth for dirt and misalignment
Bull gears provide largest torque multiplication enabling slow, controlled field pulling

## Slide 19
Bull Gear Open Design Rationale
Steam School Notes | 8 Crankdisk to Traction
Open gearing designed for dusty field environments
• Enclosed gearboxes would trap grit and moisture • Open gearing can be cleaned and inspected • Open gearing easily lubricated • Traction engines operate in dusty, muddy, uneven terrain • Intentional design for field durability
Open bull gear design enables maintenance and field operation in harsh conditions

## Slide 20
Traction Wheels Power Conversion
Steam School Notes | 8 Crankdisk to Traction
Wheels convert rotary motion to tractive movement
Wheel Characteristics • Large diameter provides leverage and smooth travel • Wide to distribute weight and prevent sinking • Fitted with cleats or lugs for soil grip • Built with massive hubs for gear and axle loads • Final stage of power train
Differential and Movement • Mounted on fixed rear axle • Differential allows each wheel own speed when cornering • Under heavy pulling, one wheel may slip • Under turning, one wheel rotates faster • Gearing accommodates all while delivering steady torque
Large wheels with lugs and high torque create slow, powerful, unstoppable movement

## Slide 21
Hitch and Drawbar Load Path
Steam School Notes | 8 Crankdisk to Traction
Load routed through cannon bearing, not boiler
Correct Load Path • Plow connects to hitch and drawbar bracket • Drawbar bracket tied to cannon-bearing structure • Lower cannon bearing carries rear axle • Axle structure supports hornplates • Hornplates connect to engine frame • Boiler not part of this chain
• Draft forces pass through axle and hornplates only • No bending moment applied to boiler barrel • Firebox and stays remain undistorted • Boiler maximum allowable working pressure protected
Load path routing preserves boiler as pressure vessel isolated from mechanical strain

## Slide 22
Why Boiler Cannot Carry Hitch Load
Steam School Notes | 8 Crankdisk to Traction
Boiler weak in bending and external point loads
Boiler Strength Profile • Strong in internal pressure tension • Weak in bending stress • Weak in twisting stress • Weak in external point loads • Vulnerable to frame-type stresses • Riveted shells especially susceptible to distortion
Distortion Consequences • Small deflections misalign crankshaft and gearing • Distorts firebox sheets • Overstresses stays • Reduces maximum allowable working pressure • Causes leaks at seams and rivet lines
Boiler must not be used as structural member or subjected to bending, twisting, or external mechanical loads

## Slide 23
Boiler Design Principle
Steam School Notes | 8 Crankdisk to Traction
Boiler is pressure vessel, not structural frame
• Boiler designed as enclosed pressure vessel • Not designed to carry external mechanical loads • Cannot withstand bending or twisting • Cannot tolerate structural frame stresses • Principle established in traction-engine era • Explicit in modern historical-boiler regulations
Any bending, twisting, or external mechanical load can distort seams, stays, or firebox sheets and reduce safe working pressure
Boiler pressure-vessel design principle is fundamental and non-negotiable

## Slide 24
Plowing Engine Drawbar Loads
Steam School Notes | 8 Crankdisk to Traction
Plowing engines experience extreme continuous loads
• Continuous high drawbar load during plowing • Shock loads from soil engagement and exit • Long periods of sustained high torque • Uneven ground and side loads • Far greater than road haulage loads
• If transmitted to boiler, could distort pressure vessel • Distortion reduces safe operating pressure • Could cause structural damage to boiler • Routing through cannon bearing and hornplates ensures safe operation
Plowing loads far exceed haulage; cannon bearing routing enables safe full-power pulling