## Slide 1
Steering Wheel to Front Axle
Steam School Notes | 9 Steering Wheel to Front Axle
Traction engine steers by swinging entire front axle
• Unlike automobiles, individual front wheels do not pivot on steering knuckles • The entire front axle assembly swings for steering control • Steering gear provides mechanical advantage for smooth, accurate control

## Slide 2
Steering Wheel
Steam School Notes | 9 Steering Wheel to Front Axle
Large wheel provides operator leverage
• Steering system is heavily geared down • Wheel must turn many revolutions to swing front axle from lock to lock • Size gives mechanical advantage for control

## Slide 3
Steering Shaft
Steam School Notes | 9 Steering Wheel to Front Axle
Shaft connects wheel to worm gear
• Runs diagonally down toward front of engine • Supported in bearings • Ends in worm gear at bottom

## Slide 4
Worm Gear
Steam School Notes | 9 Steering Wheel to Front Axle
Worm engages with worm wheel or segment
• Provides very high mechanical advantage • Enables slow, controlled steering • Self-locking action prevents front wheels from kicking back
• Located at bottom of steering shaft • Turns the chain roll

## Slide 5
Chain Roll (Steering Drum)
Steam School Notes | 9 Steering Wheel to Front Axle
Drum converts worm rotation to chain pull
• Horizontal drum with grooves or flanges to guide steering chain • One side of chain winds in as other side pays out • Converts worm's rotation into controlled pull on steering chains

## Slide 6
Steering Chains
Steam School Notes | 9 Steering Wheel to Front Axle
Chains pull front axle through steering springs
• Run from chain roll down to front axle • Pull directly on axle through steering springs • Winding left chain and paying out right chain turns axle left • Reversing drum direction turns axle right

## Slide 7
Steering Springs
Steam School Notes | 9 Steering Wheel to Front Axle
Springs protect system and ensure smooth control
• Keep chain tensioned • Absorb shocks from rough ground • Prevent sudden jerks from reaching worm gear • Allow axle to rock without slackening chain
• Located between chain and axle • Ensure smooth, quiet steering • Protect the gearing from damage

## Slide 8
Front Axle Assembly
Steam School Notes | 9 Steering Wheel to Front Axle
Axle performs horizontal and vertical motions
• Horizontally, for steering—entire axle swings left or right as unit • Vertically, to follow uneven terrain—axle rocks up and down around central pivot pin
• Dual-pivot action keeps both front wheels on ground over bumps and ruts • Allows engine to steer while maintaining ground contact

## Slide 9
Pedestal (Front Axle Pivot)
Steam School Notes | 9 Steering Wheel to Front Axle
Heavy casting anchors entire steering system
• Located at front of engine • Carries axle pivot pin • Supports weight of front of engine • Supports side loads from steering • Supports rocking motion of axle over uneven ground
• Structural anchor for entire steering system • Heavy casting provides necessary support and rigidity

## Slide 10
Reach
Steam School Notes | 9 Steering Wheel to Front Axle
Member connects pedestal to boiler and hornplates
• Keeps pedestal aligned with engine frame • Carries fore-and-aft loads from steering and road shocks • Prevents pedestal from twisting or shifting • Maintains correct geometry between front and rear axles
• Long structural member • Provides structural reference for pedestal without it, pedestal would have no structural reference to rest of engine

## Slide 11
Steering System Summary
Steam School Notes | 9 Steering Wheel to Front Axle
Worm-and-chain mechanism provides shock-free control
Load Path • Steering Wheel • Steering Shaft • Worm Gear • Chain Roll • Steering Chains • Steering Springs • Front Axle (horizontal + vertical pivot) • Pedestal • Reach • Hornplates
• System provides slow, powerful, shock-free control • Simple and durable design • Perfectly suited to heavy, low-speed work of steam traction engine
Steering system is simple, durable, and perfectly suited to the heavy, low-speed work of a steam traction engine