## Slide 1
Approach & Situational Awareness
Steam School Notes | Chapter 24 Cold Walk‑Up Checklist
Verify engine condition and site safety before inspection
• Engine shows no pressure on gauge and no warmth at fittings • Engine is on stable ground with brakes set or wheels chocked • Surroundings are clear of loose tools, fuel containers, and bystanders

## Slide 2
Boiler Exterior & Shell Inspection
Steam School Notes | Chapter 24 Cold Walk‑Up Checklist
Examine boiler barrel, firebox, and smokebox for damage
• Cracks, bulges, fresh rust streaks, or weeping seams • Loose or missing stays, rivets, or fasteners • Smokebox door fit and hinge condition • Stack is clear of obstructions

## Slide 3
Water Level & Feedwater System
Steam School Notes | Chapter 24 Cold Walk‑Up Checklist
Confirm gauge glass function and water feed mechanisms
• Gauge glass is intact with valves open and drains functional • Blow down gauge glass: water level responds and top/bottom cocks are clear • Try cocks provide correct water/steam response • Injector overflow pipe is clear and water supply valve moves freely • Mechanical or crosshead pump moves freely

## Slide 4
Fittings & Valves
Steam School Notes | Chapter 24 Cold Walk‑Up Checklist
Verify safety valve, throttle, and steam control mechanisms
• Safety valve easing lever moves freely • Blowdown valve is closed with sound threads • Throttle has full travel and smooth operation • Whistle valve, blower valve, and cylinder cocks move freely • Pressure gauge glass is unbroken with pointer at zero

## Slide 5
Lubrication — Before Any Motion
Steam School Notes | Chapter 24 Cold Walk‑Up Checklist
Service all oil systems and lubrication points before engine starts
• Displacement lubricators filled with correct cylinder oil • Mechanical lubricators checked for oil level, ratchet/pawl engagement, and free rotation
Oil all motion points • Crossheads, slide bars, valve gear joints • Eccentrics, crank pins, main bearings • All drip cups and wicks inspected for proper feed

## Slide 6
Motion Work & Running Gear
Steam School Notes | Chapter 24 Cold Walk‑Up Checklist
Inspect and test mechanical linkages and running components
• Flywheel turned slightly by hand to detect binding, resistance, or loose components • Connecting rods, valve rods, eccentric straps, steering gear examined • Differential and final drive inspected • Wheel hubs and axle bearings checked for oil and tightness

## Slide 7
Firebox, Grate & Ashpan
Steam School Notes | Chapter 24 Cold Walk‑Up Checklist
Clear firebox and ashpan to prepare for combustion
• Grate is in good condition with no clinker buildup or foreign objects • Ashpan is empty with no smoldering material • Ashpan damper moves freely • Fusible plug is present and not weeping

## Slide 8
Draft Path & Tubes
Steam School Notes | Chapter 24 Cold Walk‑Up Checklist
Clear smokebox and boiler tubes of soot and debris
• Smokebox is not packed with soot or ash • All tubes are clear of soot and obstructions using appropriate brushes • Blower ring is free from blockage • Damper and ashpan air controls operate smoothly

## Slide 9
Fuel & Water Readiness
Steam School Notes | Chapter 24 Cold Walk‑Up Checklist
Confirm adequate fuel and water supplies are available
• Water supply is adequate for raising steam and operating period • Fuel (coal or wood) is staged safely and adequate • Fire tools are present and in good condition

## Slide 10
Pre‑Light‑Off Final Checks
Steam School Notes | Chapter 24 Cold Walk‑Up Checklist
Complete final verification before lighting the fire
• Water level is at proper starting height • All lubrication points are serviced • Cylinder cocks, throttle, and blower are in correct starting positions • Firebox and ashpan are clear • No loose tools on footplate or running boards • Operator has PPE: gloves, eye protection, hearing protection
Engine is ready for light‑off when all checklist items are complete.