## Slide 1
Throttle Identification
Steam School Notes | 25.1 Throttle
Throttle controls power output, not speed directly
• Identify the throttle and its direction of travel • Throttle is the primary control for starting, modulating, and stopping motion

## Slide 2
Throttle Operation
Steam School Notes | 25.1 Throttle
Open throttle smoothly and progressively
• Practice smooth, progressive opening • Never snap the throttle open

## Slide 3
Governor Function
Steam School Notes | 25.2 Governor
Governor limits maximum engine speed when running
• Governor does not start the engine • Governor only trims speed once running • Governor responds to load changes
Governor cannot prevent overspeed if throttle is opened too far

## Slide 4
Dead Centre Positions
Steam School Notes | 25.3 Dead Centres
Engine cannot start when crank is on dead centre
• Front dead centre and back dead centre are crank positions • Practice identifying dead centre by crank position

## Slide 5
Rocking Off Dead Centre
Steam School Notes | 25.3 Dead Centres
Rock engine off dead centre using clutch or bar
• Use clutch to disengage and re-engage • Use rocking bar to manually move crank

## Slide 6
Cylinder Drain Cocks
Steam School Notes | 25.4 Cylinder Drains
Open drains before starting to clear condensate and prevent water hammer
• Locate cylinder drain cocks and their handles • Keep drains open until engine turns freely and dry steam appears

## Slide 7
Drain Operations
Steam School Notes | 25.4 Cylinder Drains
Use drains when stopping and maneuvering at low speed
• Open drains to clear condensate during shutdown • Open drains during low-speed maneuvering

## Slide 8
Motion Prediction
Steam School Notes | 25.5 Predicting Motion
Predict engine direction before opening throttle
• Review crank position, valve gear setting, and rotation direction • Visualize the first quarter-turn of motion • Engine may move unexpectedly if throttle is cracked too quickly

## Slide 9
Clutch Function
Steam School Notes | 25.6 Clutch
Clutch connects crankshaft to traction gearing
• Identify the clutch lever and its travel • Ensure clutch is fully engaged before applying power

## Slide 10
Clutch Engagement and Disengagement
Steam School Notes | 25.6 Clutch
Disengage clutch for maneuvering, stopping, and rocking
• Disengage when maneuvering • Disengage when stopping • Disengage when rocking off dead centre • Avoid slipping the clutch except when absolutely necessary

## Slide 11
Hooking Up Purpose
Steam School Notes | 25.7 Hooking Up (Valve Gear Adjustment)
Hooking up reduces steam consumption and enables finer speed control
• Reduces steam consumption • Provides finer control at speed • Hook up only when engine is running smoothly

## Slide 12
Hooking Up Procedure
Steam School Notes | 25.7 Hooking Up (Valve Gear Adjustment)
Hooking up changes valve events and affects starting torque
• Identify the reach rod or quadrant lever and its direction of travel • Recognize that hooking up changes valve events • Recognize that hooking up affects starting torque

## Slide 13
Stopping Steps
Steam School Notes | 25.8 Stopping Procedure
Close throttle smoothly and open drains as engine slows
• Close the throttle smoothly, never snap it shut • Open cylinder drains as engine slows to clear condensate • Disengage clutch once engine is nearly stopped

## Slide 14
Engine Securing
Steam School Notes | 25.8 Stopping Procedure
Secure the engine with throttle closed, drains open, and clutch disengaged
• Throttle closed • Drains open • Clutch disengaged • Wheels chocked if on grade
Avoid leaving the crank on dead centre if a restart is expected