## Slide 1
Purpose of Emergency Training
Steam School Notes | Chapter 27: Emergency Procedures
Emergency procedures develop automatic responses under pressure
• Practice makes correct response automatic • Safety of people comes first • Protection of equipment comes second • When in doubt: stop engine, monitor water level, seek assistance

## Slide 2
Emergency Stop
Steam School Notes | Chapter 27: Emergency Procedures
Bring engine to immediate stop when hazard enters path
• Close the throttle immediately • Move reversing quadrant into reverse • Open throttle briefly to admit short steam shot • Close the throttle immediately • Keep both hands on controls and remain on footplate until complete stop

## Slide 3
Emergency Stop Training
Steam School Notes | Chapter 27: Emergency Procedures
Gentle stops with clutch disengaged build muscle memory safely
• Full emergency stop stresses engine, gearing, transmission • Routine training uses gentler stops with clutch disengaged • Reduces wear while building muscle memory • Sequence of motions must become automatic • In real emergency, no time to think step-by-step
When imminent hazard exists, safety of people takes precedence over mechanical strain or equipment wear

## Slide 4
Emergency Stop Common Errors
Steam School Notes | Chapter 27: Emergency Procedures
Common mistakes during emergency stop procedures
• Hesitating before closing the throttle • Failing to move fully into reverse • Applying reverse steam for too long • Focusing on engine rather than hazard • Forgetting to close throttle after reverse steam

## Slide 5
Water Glass Inspection
Steam School Notes | Chapter 27: Emergency Procedures
Inspect water glass before each startup procedure
• Check for cracks, chips, or other damage • Pay attention to areas near upper and lower retaining nuts • Verify water and steam valves operate freely • Confirm try cocks are functional and accessible

## Slide 6
Broken Water Glass Indications
Steam School Notes | Chapter 27: Emergency Procedures
Broken water glass shows sudden steam and water release
• Sudden release of steam and water from water column • Cloud of steam around engineer's position • Loss of visibility near water glass • Inability to determine boiler water level from glass

## Slide 7
Broken Water Glass Protection Equipment
Steam School Notes | Chapter 27: Emergency Procedures
Carry shovel or board to shield from escaping steam and water
• Short-handled shovel for emergency use on every engine • Wide board from wood supply may serve as protective shield • Equipment required even when operating on fuels other than coal

## Slide 8
Broken Water Glass Response
Steam School Notes | Chapter 27: Emergency Procedures
Close water valve before steam valve to minimize discharge
• Put on gloves and available personal protective equipment • Approach cautiously using shovel or board as shield • Close the water valve • Close the steam valve
• Hot water presents greater burn hazard than escaping steam • Closing water valve first reduces discharge of hot boiler water • Then isolate steam side of gauge

## Slide 9
Broken Water Glass Water Level Confirmation
Steam School Notes | Chapter 27: Emergency Procedures
Use try cocks to confirm actual boiler water level
• Engineer should understand boiler water level through regular observation • Water level must be confirmed after water glass isolation • Use try cocks to determine actual boiler water level • Proceed before continuing operation or further action

## Slide 10
Broken Water Glass Important Notes
Steam School Notes | Chapter 27: Emergency Procedures
Monitor water level with alternate methods until repairs complete
• Continue monitoring boiler water using approved alternate methods • Procedure assumes side-mounted water column and glass • Operators must understand specific engine arrangement • Adjust procedure as required for engine design • Test try cocks regularly during normal operation • Become familiar with try cock indications before emergency

## Slide 11
Broken Water Glass Common Errors
Steam School Notes | Chapter 27: Emergency Procedures
Common mistakes when responding to broken water glass
• Failing to inspect glass before operation • Approaching failed glass without protection • Closing steam valve before water valve • Assuming water level without verification • Forgetting different engine designs require modified procedure

## Slide 12
Low Water Emergency Indications
Steam School Notes | Chapter 27: Emergency Procedures
Recognize low water by absence of water on glass and try cocks
• Water disappearing from water glass • No water showing on try cocks • Uncertainty about actual water level • Failure of feedwater equipment with falling water level
A low-water condition is the fundamental emergency for boiler operators

## Slide 13
Low Water Emergency Response
Steam School Notes | Chapter 27: Emergency Procedures
Stop engine and safe fire immediately in low water condition
• Stop the engine • Safe the fire • Do not leave boiler unattended • Monitor situation and seek assistance from experienced crew
When in doubt, stop the engine and treat the situation as low-water emergency until proven otherwise

## Slide 14
Low Water Common Errors
Steam School Notes | Chapter 27: Emergency Procedures
Common mistakes in low water emergency response
• Becoming distracted from water-level duties • Ignoring steadily falling water level • Delaying action when water level becomes uncertain • Assuming someone else is monitoring boiler

## Slide 15
Injector Failure Indication
Steam School Notes | Chapter 27: Emergency Procedures
Injector failure means no pickup, no delivery, or unsteady feed
• Injector will not pick up water • Injector will not deliver water to boiler • Injector will not maintain steady feed • First confirm water exists in tender

## Slide 16
Injector Overheating Causes
Steam School Notes | Chapter 27: Emergency Procedures
Injector overheating prevents water pickup and operation
• Faulty injector check valve allowing hot water backflow • Faulty feedwater-line check valve allowing hot water backflow • Leaking steam throttle valve heating injector when idle • High ambient temperatures on hot day • Leak in suction line • Empty water tender

## Slide 17
Injector Initial Checks
Steam School Notes | Chapter 27: Emergency Procedures
Check water supply, suction line, temperature, and valve leaks
• Adequate water in tender • Obvious suction-line leaks • Excessive injector temperature • Steam or water leaks around injector fittings and valves

## Slide 18
Cooling an Overheated Injector
Steam School Notes | Chapter 27: Emergency Procedures
Wet rag cooling restores operation in many overheated cases
• Wrap rag around body of injector • Thoroughly wet rag with water, preferably cold • Continue cooling until injector temperature is reduced • Attempt to restart injector
• Wet rag draws heat away from injector • Often restores normal operation quickly

## Slide 19
Repeated Injector Overheating
Steam School Notes | Chapter 27: Emergency Procedures
Investigate underlying cause of repeated overheating events
• Defective injector check valves • Defective feedwater check valves • Leaking steam valves • Conditions allowing hot water to circulate back into injector

## Slide 20
Injector Cannot Be Restored
Steam School Notes | Chapter 27: Emergency Procedures
Use alternate feedwater source if injector fails beyond repair
• Use other available feedwater source • Continue monitoring boiler water level closely • Evaluate whether engine should remain in service • Prepare to safe fire and remove engine from operation • Every boiler requires two independent feedwater means

## Slide 21
Injector Failure Common Errors
Steam School Notes | Chapter 27: Emergency Procedures
Common mistakes in injector troubleshooting and operation
• Assuming injector is mechanically damaged before checking for overheating • Forgetting to verify water level in tender • Ignoring suction-line leaks • Failing to investigate cause of repeated overheating • Continuing operation without reliable feedwater means

## Slide 22
Boiler Overfill Symptoms
Steam School Notes | Chapter 27: Emergency Procedures
Overfilled boiler compromises water glass reliability
• Water glass becomes sluggish or unresponsive • Small pocket of trapped air at top of water glass • Indicated water level no longer accurately represents true level

## Slide 23
Boiler Overfill Recovery
Steam School Notes | Chapter 27: Emergency Procedures
Lower water level until water glass becomes responsive
• Reduce boiler water level carefully using blowdown • Lower water level only until glass becomes responsive • Restore reliable indication of boiler water level • Continue normal monitoring of water glass and try cocks

## Slide 24
Boiler Overfill Prevention
Steam School Notes | Chapter 27: Emergency Procedures
Maintain constant attention while feeding water to boiler
• Keep one hand on steam-side injector valve while feeding • Do not remove hand until injection is complete • Watch water glass continuously • When injecting, do nothing else
For novice operators, a simple rule applies: when injecting, do nothing else

## Slide 25
Governor Belt Failure
Steam School Notes | Chapter 27: Emergency Procedures
Governor failure allows engine to accelerate to dangerously high speeds
• Sudden increase in engine speed • Visible failure or loss of governor belt • Governor no longer responds to speed changes • Unusual engine behavior requiring immediate throttle control
Governor failure should always be treated as serious event regardless of current work

## Slide 26
Governor Belt Failure Response
Steam School Notes | Chapter 27: Emergency Procedures
Close throttle immediately and bring engine to complete stop
• Close throttle immediately • Bring engine to complete stop • Secure engine and assess situation before resuming operation

## Slide 27
Post-Governor Failure Inspection
Steam School Notes | Chapter 27: Emergency Procedures
Inspect for damage after engine overspeed event
• Inspect governor belt and governor components • Check for visible damage to moving parts • Roll engine over slowly by hand • Listen for unusual knocks, impacts, or new mechanical noises

## Slide 28
Governor Failure with Suspected Damage
Steam School Notes | Chapter 27: Emergency Procedures
Remove engine from service if damage or safety concerns exist
• Remove engine from service immediately • Safe the fire • Continue monitoring boiler water level • Arrange for engine towing to yard or repair facility

## Slide 29
Governor Failure Without Damage
Steam School Notes | Chapter 27: Emergency Procedures
Engine can operate without governor with crew caution and attention
• Repair governor belt in field • Fabricate replacement governor belt in nearby shop • Continue operation without governor • Drive engine back to yard without governor • Requires constant attention to throttle position and engine speed

## Slide 30
Governor Failure Decision Making
Steam School Notes | Chapter 27: Emergency Procedures
Consult with experienced operators to determine best course of action
• Consult with engine crew • Consult with nearby operators • Consult with event organizers or operating supervisors • Determine safest option: repair, restricted operation, towing, or removal • Show engines perform non-critical work, accept no safety doubt

## Slide 31
Governor Failure Common Errors
Steam School Notes | Chapter 27: Emergency Procedures
Common mistakes in governor failure emergency response
• Delaying throttle closure • Continuing operation without inspecting for damage • Assuming overspeed caused no harm • Becoming distracted while operating without governor • Continuing operation when repair or towing would be safer

## Slide 32
Grass Fire Prevention
Steam School Notes | Chapter 27: Emergency Procedures
Situational awareness is most important fire prevention tool
• Watch for dry grass, straw, and stubble near engine • Pay attention to area beneath ash pan when stopping • Stop on plowed ground rather than standing stubble • Ensure suitable firefighting equipment available before operations
Steam engines operate around dry vegetation, hot ash, sparks, and open fire

## Slide 33
Grass Fire Equipment
Steam School Notes | Chapter 27: Emergency Procedures
Firefighting equipment required depends on activity and location
• Water barrels with buckets • Water wagon equipped with pump • Shovels for smothering small fires with soil

## Slide 34
Grass Fire Response
Steam School Notes | Chapter 27: Emergency Procedures
Stop on safe surface and close draft to reduce airflow through fire
• Stop engine in safe location • Stop on plowed ground, bare soil, or non-combustible surface if possible • Close draft to reduce airflow through fire and ash pan • Determine source of fire • Extinguish fire using available equipment • Inspect area for remaining hot spots before resuming operation

## Slide 35
Grass Fire Extinguishing Methods
Steam School Notes | Chapter 27: Emergency Procedures
Use soil for small fires and firefighting equipment for larger fires
• Small grass or stubble fires: use loose soil to smother flames • This is why every engine should carry a shovel • Larger fires: use firefighting equipment available at site • If closing draft does not reduce ash-pan fire, examine draft doors

## Slide 36
Grass Fire Common Errors
Steam School Notes | Chapter 27: Emergency Procedures
Common mistakes when responding to grass fire emergency
• Stopping in dry grass while responding to grass fire • Failing to monitor ground conditions around engine • Leaving area before confirming fire is completely extinguished
Stop on the plowed part, not the grass

## Slide 37
When in Doubt: General Principles
Steam School Notes | Chapter 27: Emergency Procedures
Follow established principles when facing unfamiliar emergency situation
• Stop the engine • Maintain awareness of boiler water level • Safe the fire if necessary • Consult experienced crew members • Do not continue operation until situation is understood
No emergency chapter can anticipate every problem encountered around a steam engine