## Slide 1
Isolation Valves Overview
Steam School Notes | Chapter 4: Isolation Valves
Check valve positions before operating boiler
• Valves change position, especially in museum settings with many hands • Always verify valve positions before approaching boiler for operation

## Slide 2
Purpose of Isolation Valves
Steam School Notes | Chapter 4: Isolation Valves
Isolation valves enable component service without depressurizing boiler
• Allow fitting, line, or accessory removal from service without dropping boiler pressure • Enable isolation of component for proving, cleaning, repair, or replacement • Keep rest of boiler fully pressurized and in water during maintenance • Located at boiler end of any line requiring occasional service

## Slide 3
Isolation Valve Requirements
Steam School Notes | Chapter 4: Isolation Valves
Isolation valves must meet five critical requirements
• Withstand full boiler pressure • Withstand steam temperature • Seal positively when closed • Be fully open in normal operation • Be located as close to boiler shell as practical
• Valve unsuitable for isolation duty if unable to meet any requirement

## Slide 4
Isolation Valve Location
Steam School Notes | Chapter 4: Isolation Valves
Install isolation valves as close to boiler shell as practical
• Closing valve exposes only short pipe length or single fitting • Marks boundary between boiler proper and serviceable plumbing
• Steam and water isolation valves for gauge glass • Turret isolation valve feeding accessory manifold • Injector steam and water isolation valves • Blower isolation valve • Blowdown valve at lowest boiler point

## Slide 5
Valve Position During Operation
Steam School Notes | Chapter 4: Isolation Valves
All isolation valves must be fully open during normal steaming
• Each device sees true boiler pressure and unrestricted flow when valve fully open • Gauge glass with either isolation valve shut will give false reading • Injector with steam or water valve partly closed will not pick up • Blower or turret line with isolation valve shut will appear dead
• Open during normal service • Closed only when isolating component for maintenance, proving, or safety

## Slide 6
Locating Isolation Valves
Steam School Notes | Chapter 4: Isolation Valves
Isolation valves located at fixtures connected to steam or water space
• Check isolation valves by considering each plumbing section • Isolation valve exists at closest boiler point for each connected fixture

## Slide 7
Injector Isolation Valves
Steam School Notes | Chapter 4: Isolation Valves
Injectors require two isolation valves at boiler connection points
• Feedwater entry isolation valve • Steam supply isolation valve

## Slide 8
Main Steam Line Isolation Valve
Steam School Notes | Chapter 4: Isolation Valves
Main steam line isolation valve located at dome
• Single isolation valve point for main steam distribution

## Slide 9
Water Column Isolation Valves
Steam School Notes | Chapter 4: Isolation Valves
Water column has two isolation valves for independent isolation
• Steam side isolation valve • Water side isolation valve

## Slide 10
Blower Isolation Valve
Steam School Notes | Chapter 4: Isolation Valves
Blower isolation may depend on injector steam supply configuration
• On some engines, blower fed from injector steam supply • Blower isolation tied to injector isolation on these engines