## Slide 1
Types of Lubricators
Steam School Notes | Chapter 5: Lubrication Points
Recognize lubricator types on warm engines
• Fittings are small, varied, and resemble ordinary hardware • Identification requires knowing lubricator type and function • Each type delivers different lubricant to specific locations

## Slide 2
Oil Cups
Steam School Notes | Chapter 5: Lubrication Points
Oil cups deliver light machine oil by gravity
• Small upright cups with cap or flip-lid • Knurled knob controls drip rate • Lever flips to turn off oil entirely • Found: main bearings, crank pins, valve-gear pivots, governor bearings

## Slide 3
Screw-down Grease Cups
Steam School Notes | Chapter 5: Lubrication Points
Screw-down grease cups force grease into slow-moving bearings
• Filled with hard grease • Screw cap down one turn to force grease into bearing • Found: steering gear, axle bearings, some valve-gear joints • Short, squat cup with threaded cap that screws downward

## Slide 4
Mechanical Lubricators
Steam School Notes | Chapter 5: Lubrication Points
Mechanical lubricators deliver measured oil strokes driven by engine motion
• Ratchet or displacement type • Found: cylinder lubrication, governor drive, high-load bearings • Recognition: small box with ratchet arm or linkage; oil lines leading away

## Slide 5
Hydrostatic Lubricators
Steam School Notes | Chapter 5: Lubrication Points
Hydrostatic lubricators feed cylinder oil using steam pressure and sight glass
• Sight-feed lubricators with glass column and needle valve • Feed lines visible; usually mounted on turret • Found: cylinder lubrication on many engines; water pumps • See drops through sight glass

## Slide 6
Alemite/Zerk Fittings
Steam School Notes | Chapter 5: Lubrication Points
Alemite and Zerk fittings are modern grease nipple retrofits
• Small conical or ball-type grease nipples • Found: anywhere previous owner wanted easier greasing • Modern retrofits replacing original lubricators

## Slide 7
Wick Lubricators
Steam School Notes | Chapter 5: Lubrication Points
Wick lubricators meter oil slowly through felt or cotton wick
• Felt or cotton wick meters oil slowly • Found: valve rocker arm, upper and lower cannon bearings • Reservoir in casting filled with cotton waste

## Slide 8
Cylinder Oil
Steam School Notes | Chapter 5: Lubrication Points
Cylinder oil is very heavy, high-temperature oil for steam contact
• Used only where steam enters (cylinders, valves) • Formulated to dissolve in water • Delivered by hydrostatic or mechanical lubricators

## Slide 9
Engine Oil
Steam School Notes | Chapter 5: Lubrication Points
Engine oil is medium-weight light machine oil for bearings and joints
• Used for bearings, pins, and moving joints • Delivered by oil cups, wicks, or mechanical lubricators

## Slide 10
Grease for Bearings
Steam School Notes | Chapter 5: Lubrication Points
Grease lubricates slow, high-load bearings
• Delivered by grease cups or Zerk fittings

## Slide 11
Matching Lubricant to Lubricator
Steam School Notes | Chapter 5: Lubrication Points
Wrong lubricant with wrong lubricator is as bad as missing the point
Matching the wrong lubricant to the wrong lubricator is as bad as missing the point entirely

## Slide 12
Cold Engine Lubrication Challenge
Steam School Notes | Chapter 5: Lubrication Points
Cold engines require manual oiling because self-lubrication systems fail to function
• Oil is thick when engine is cold • Grease is stiff when engine is cold • Wicks don't draw when engine is cold • Mechanical lubricators may not stroke when engine is cold • Hydrostatic lubricators won't feed until steam is up

## Slide 13
Manual Oiling During Warm-up
Steam School Notes | Chapter 5: Lubrication Points
Operators hand-oil every point during warm-up because automatic systems are inactive
• Know where each point is located • Know what type of lubricator it uses • Know what lubricant belongs there • Know whether it needs manual priming before engine moves
Experienced operators walk the engine with an oil can during warm-up knowing exactly what they are looking at