## Slide 1
Introduction
Steam School Notes | 23 Measurement of Power
Power is the rate at which work is performed
• Steam age engineers compared engines and evaluated performance • Early engines replaced horses in mines, mills, and pumping stations • Thomas Savery promoted steam engines as horse replacements in 1702
James Watt formalized horsepower comparison by defining one mechanical horsepower as 33,000 foot-pounds of work per minute.

## Slide 2
Horsepower Definition
Steam School Notes | 23 Measurement of Power
One mechanical horsepower equals 550 foot-pounds per second
• Raise 33,000 pounds one foot high in one minute • Raise 330 pounds 100 feet high in one minute • Perform any equivalent work amount at the same rate
• 1 hp = 550 ft·lb/s • 1 hp = 33,000 ft·lb/min

## Slide 3
Multiple Horsepower Definitions
Steam School Notes | 23 Measurement of Power
Several different horsepower definitions exist depending on what is measured
• Electrical horsepower: 746 watts of electrical power • Boiler horsepower: boiler's ability to generate steam • Indicated horsepower: power developed in engine cylinders • Brake horsepower: power available at engine shaft • Drawbar horsepower: useful pulling power at locomotive drawbar
Steam engineers must verify which horsepower definition applies, since two machines with the same rating may measure different quantities.

## Slide 4
Horsepower vs. Actual Horse Power
Steam School Notes | 23 Measurement of Power
Watt's horsepower is a standard unit, not measured from actual horses
• Actual horse power varies by size, conditioning, duration, and ground conditions • Practical tasks often required teams of multiple horses • Standard unit allows machines and animals to be compared on common scale

## Slide 5
Drawbar Horsepower Measurement
Steam School Notes | 23 Measurement of Power
Drawbar horsepower measures power delivered through the drawbar when pulling a load
• Measured by pulling force at drawbar and speed • Power equals product of force and velocity
• hp_d = (F × v) / 375 • F = drawbar pull (lb) • v = speed (mph) • Constant 375 derived from Watt's definition

## Slide 6
Drawbar Horsepower Example
Steam School Notes | 23 Measurement of Power
Calculate drawbar horsepower from measured force and speed
• Tractor drawbar pull: 2,025 pounds • Speed: 5 miles per hour • hp_d = (2,025 × 5) / 375 = 27 hp

## Slide 7
Pulley Horsepower
Steam School Notes | 23 Measurement of Power
Pulley horsepower measures power delivered through belt pulley for stationary machinery
• Power lost in gears, bearings, wheels, wheel slip, and rolling resistance • Drawbar horsepower always less than shaft power • Same machine may have different pulley and drawbar horsepower ratings

## Slide 8
Marketing Power Designations
Steam School Notes | 23 Measurement of Power
Traction engines commonly carried two power ratings for marketing purposes
Example Rating | First Number | Second Number
Case 18–50 | Boiler horsepower | Belt (pulley) horsepower
Case 22–65 | Boiler horsepower | Belt (pulley) horsepower
Case 28–80 | Boiler horsepower | Belt (pulley) horsepower
Horsepower ratings in advertisements and nameplates must be interpreted carefully, as they may refer to boiler, indicated, brake, pulley, or drawbar horsepower.

## Slide 9
Winnipeg Tractor Trials
Steam School Notes | 23 Measurement of Power
Scientific testing methods allowed independent verification of engine performance
• Held between 1908 and 1913 in Winnipeg • Originally conceived as industrial exhibition • Agricultural researchers introduced scientific testing and standardized measurements • Forerunner of Nebraska Tractor Tests after World War I
Independently verified performance figures carried more weight than advertising claims.

## Slide 10
De Prony Brake Development
Steam School Notes | 23 Measurement of Power
Gaspard de Prony invented the de Prony brake to measure torque from a rotating shaft
• Described in 1826 by French engineer Gaspard Clair François Marie Riche de Prony • Measured torque produced by rotating shaft • Widely used throughout nineteenth and early twentieth centuries

## Slide 11
De Prony Brake Operation
Steam School Notes | 23 Measurement of Power
Friction brake converts engine torque into measurable force and distance
• Friction brake wrapped around rotating drum or flywheel • Lever arm resists brake motion • Force measured using scale or force-measuring device • Converts torque into force and distance

## Slide 12
Torque Calculation
Steam School Notes | 23 Measurement of Power
Torque equals force multiplied by the lever arm length
• T = F · L • T = torque • F = measured force (lb) • L = length of brake arm (ft)

## Slide 13
Brake Horsepower Formula
Steam School Notes | 23 Measurement of Power
Engine power can be determined from torque measurement and rotational speed
• Distance per revolution = 2πL • Work per minute = F · 2πL · r • Horsepower = (F · L · r) / 5,252 • L = brake-arm length (ft) • r = rotational speed (rpm) • F = measured force (lb)
A simple scale, lever arm, and tachometer allowed engineers to determine brake horsepower accurately.

## Slide 14
Simplified Brake Horsepower
Steam School Notes | 23 Measurement of Power
A brake arm length of 63 inches simplifies horsepower calculation dramatically
• Arm length exactly 63 inches (5.25 ft) • Produces convenient relationship: hp = (r · F) / 1,000 • At 250 rpm, each 4 pounds equals approximately 1 horsepower
The convenient shortcut allowed field test officials to determine engine power quickly without extensive calculation.

## Slide 15
De Prony Brake Historical Impact
Steam School Notes | 23 Measurement of Power
De Prony brake transformed horsepower from advertising claim to measurable quantity
• Enabled objective comparison of competing machines • First time engines compared using objective engineering data • Replaced reputation and advertising-based comparisons
Independent verification via de Prony brake demonstrated that manufacturers' advertising claims could be verified objectively.

## Slide 16
Torque vs. Horsepower
Steam School Notes | 23 Measurement of Power
Torque and horsepower are related but measure different physical quantities
Quantity | Definition
Torque | Twisting force applied at end of wrench
Horsepower | Rate at which work is performed
• Engine producing large torque at low speed may equal smaller torque at high speed • Both may produce same horsepower • Torque answers: How hard is it pushing? • Horsepower answers: How fast is work being done?
At zero speed, horsepower is zero regardless of torque produced, since power is the rate of doing work.

## Slide 17
De Prony Brake Practical Details
Steam School Notes | 23 Measurement of Power
Large horsepower measurements generate heat requiring lubrication and cooling
• Beef tallow used as lubricant for brake band • Modern brakes use hollow brake wheel resembling steel tire • Cooling water continuously introduced into wheel • Centrifugal force distributes water inside rotating wheel • Internal pickup collects water for disposal
A 100-horsepower engine delivers approximately 255,000 BTU per hour to the brake, nearly all of which must be removed as heat.

## Slide 18
Indicated Horsepower
Steam School Notes | 23 Measurement of Power
Indicated horsepower estimates power produced by the piston using steam indicator measurements
• Alternative to de Prony brake measurement • Steam indicator measures pressure within cylinder • Indicator diagram provides average pressure on piston • Power estimated directly from cylinder measurements

## Slide 19
Force and Work Calculation
Steam School Notes | 23 Measurement of Power
Indicated horsepower calculated from pressure, area, stroke, and speed
• Force = Pressure × Area • Work = Force × Distance • Horsepower = Work multiplied by strokes per minute

## Slide 20
Boiler Pressure vs. Cylinder Pressure
Steam School Notes | 23 Measurement of Power
Boiler pressure gauge reading differs from actual pressure acting on piston
• Steam passes through dry pipe, throttle, governor, steam chest, valve passages • Each restriction causes pressure drop • Engineers call losses wire drawing • Cylinder pressure generally lower than boiler gauge pressure • Indicator card records actual piston pressure
Indicator card reveals actual pressure reaching the piston, while boiler gauge shows available pressure.

## Slide 21
PLAN Formula
Steam School Notes | 23 Measurement of Power
Indicated horsepower estimated using PLAN formula for simple geometric approximation
• HP = PLAN / 33,000 • P = Effective cylinder pressure (psi) • L = stroke length (ft) • A = piston area (in²) • N = power strokes per minute

## Slide 22
Indicated Horsepower Example Setup
Steam School Notes | 23 Measurement of Power
Calculate indicated horsepower for Case 22-65 engine at specified conditions
Parameter | Value
Cylinder pressure | 100 psi
Cutoff | 33% of stroke
Stroke | 11 in
Bore | 10 in
Speed | 225 rpm

## Slide 23
Mean Effective Pressure Calculation
Steam School Notes | 23 Measurement of Power
Mean effective pressure approximated by rectangle and triangle on indicator card
• Assumption: full pressure during first one-third of stroke • Assumption: linear pressure decline to zero during remaining two-thirds • P = (1/3)Pc + (2/3)(Pc/2) • P = (2/3)Pc • For 100 psi: P ≈ 67 psi

## Slide 24
Piston Area Calculation
Steam School Notes | 23 Measurement of Power
Calculate piston area from bore diameter using circle area formula
• A = (π × B²) / 4 • For 10-inch bore: • A = (π × 10²) / 4 • A = 78.500 in²

## Slide 25
Power Strokes Calculation
Steam School Notes | 23 Measurement of Power
Double-acting engine produces two power strokes per revolution
• N = 2 × rpm • For 225 rpm: • N = 2 × 225 = 450 strokes/min

## Slide 26
Stroke Length Conversion
Steam School Notes | 23 Measurement of Power
Convert stroke length from inches to feet for PLAN formula
• L = 11 / 12 = 0.917 ft

## Slide 27
PLAN Formula Application
Steam School Notes | 23 Measurement of Power
Apply PLAN formula with calculated values to estimate indicated horsepower
• HP = PLAN / 33,000 • HP = (67 × 0.917 × 78.500 × 450) / 33,000 • HP ≈ 65.500 hp
Simple approximation of indicator diagram yielded approximately 65 horsepower, remarkably close to Case 22-65 rated output.

## Slide 28
Indicator Diagram Power Analysis
Steam School Notes | 23 Measurement of Power
Indicator diagram and engine dimensions allow surprisingly accurate power estimation
• Mean effective pressure estimated from indicator diagram • PLAN formula applied with engine dimensions • Result remarkably close to actual engine rating • Demonstrates power of indicator diagram method
Steam engineers estimated engine output with surprising accuracy using only pressure measurements, geometry, and arithmetic.

## Slide 29
Power Measurement Methods Summary
Steam School Notes | 23 Measurement of Power
Three methods measure power from different perspectives of the engine system
Method | Measures
Drawbar horsepower | Power delivered to load
Brake horsepower | Power delivered at shaft
Indicated horsepower | Power produced within cylinder
Each method tells part of the performance story.

## Slide 30
Steam Engine Analysis Achievement
Steam School Notes | 23 Measurement of Power
Steam engineers analyzed engine performance with remarkable accuracy using fundamental principles
• Indicator diagram reveals cylinder pressure variation • Geometric approximation estimates mean effective pressure • PLAN formula converts pressure to power • Accomplished without electronic sensors or computers
Long before electronic data acquisition, steam engineers estimated engine power using pressure measurements, geometry, and arithmetic.