## Slide 1
Classification
Steam School Notes | 12 Riveted Joints
Riveted joints classified by application
• Structural: bridges, beams, trusses • Pressure-tight: tanks and containers • Boiler: load-bearing and steam/water-tight

## Slide 2
Installation
Steam School Notes | 12 Riveted Joints
Rivet consists of shank with factory head
• Factory head formed at one end • Length chosen to project beyond plates • Projecting end forms field head after upsetting

## Slide 3
Installation Process
Steam School Notes | 12 Riveted Joints
Heating and upsetting creates field head
• Heat rivet and insert into prepared hole • Support factory head with bucking bar • Upset projecting end using hammer and rivet set • Displaced metal forms field head and clamps plates

## Slide 4
Installation - Cooling Effect
Steam School Notes | 12 Riveted Joints
Cooling contraction creates tensile stress in rivet
• Hot rivet cools and contracts • Rivet heads prevent shortening • Rivet placed in tension • Plates compressed together
Clamping force from cooling helps prevent leakage and transfers load by friction.

## Slide 5
Caulking
Steam School Notes | 12 Riveted Joints
Caulking tool displaces edge metal to seal gaps
• Blunt tool driven along plate edge at 15° to 18° • Edge metal forced tightly against adjoining plate • Closes leakage path

## Slide 6
Caulking Effect
Steam School Notes | 12 Riveted Joints
Caulking improves tightness but contributes little to strength
• Seams may contain more rivets than needed for strength • Additional rivets ensure satisfactory tightness • Design balances strength and leakage prevention

## Slide 7
Riveted Joint Types
Steam School Notes | 12 Riveted Joints
Two primary joint types used in boilers
• Lap joint: plates overlap, connected by single rivet row • Butt joint: plate edges meet, joined by cover straps

## Slide 8
Lap Joint Characteristics
Steam School Notes | 12 Riveted Joints
Lap joint: one plate overlaps another
• Rivets transfer load by shear • Fewer parts required • Easy to manufacture • Load path offset causes bending when loaded

## Slide 9
Butt Joint Characteristics
Steam School Notes | 12 Riveted Joints
Butt joint: edges meet and join via cover straps
• Plates remain in same plane • More direct load path than lap joint • Commonly used for important boiler seams • Cover straps called straps

## Slide 10
Single-Cover Butt Joint
Steam School Notes | 12 Riveted Joints
Cover strap on one side joins plate edges
• Single cover strap on one side • Plate edges meet

## Slide 11
Double-Cover Butt Joint
Steam School Notes | 12 Riveted Joints
Cover straps on both sides load transmission
• Cover straps on both sides • Symmetric load transmission • Stronger and more efficient than single-cover

## Slide 12
Double-Row Lap Joint
Steam School Notes | 12 Riveted Joints
Two rivet rows increase strength and tightness
• Plates overlap • Connected by two rows of rivets • Additional rivets increase strength • Additional rivets increase tightness

## Slide 13
Staggered Rivet Pattern
Steam School Notes | 12 Riveted Joints
Staggered rows reduce hole weakening effect
• Butt joint with two rivet rows • Staggered rivet arrangement • Improves joint efficiency • Reduces weakening from rivet holes

## Slide 14
Joint Dimension Variables
Steam School Notes | 12 Riveted Joints
Standard dimensions used in riveted-joint calculations
• p: pitch (rivet spacing) • m: margin (edge distance) • d: rivet diameter • p_b: back pitch (row spacing) • p_d: diagonal pitch

## Slide 15
Joint Design Tradeoffs
Steam School Notes | 12 Riveted Joints
Design balances multiple competing factors
• Strength requirements • Tightness requirements • Manufacturing cost • Ease of inspection
Additional rivet rows increase strength but require more holes, removing metal and increasing construction time.

## Slide 16
Failure Modes
Steam School Notes | 12 Riveted Joints
Riveted joints can fail in multiple ways
• Tearing of plate along section weakened by rivet holes • Shearing of the rivets • Crushing of the rivets • Crushing of plate at rivet holes or margin

## Slide 17
Joint Strength Governs Failure
Steam School Notes | 12 Riveted Joints
Weakest failure mode determines joint strength
• Each failure mode analyzed separately • Joint strength limited by weakest mode • Maximum safe load determined by smallest failure load
Good design proportions rivets, pitch, and plate thickness so no single failure mode is excessively weaker than others.

## Slide 18
Tearing of Plate
Steam School Notes | 12 Riveted Joints
Rivet holes weaken plate like perforations
• Holes remove part of metal • Narrow strip between holes resists load • Width available to resist tearing: (p - d) • Net tearing area: (p - d) × t

## Slide 19
Tearing Force Calculation
Steam School Notes | 12 Riveted Joints
Tearing force equals tensile stress times net area
• P_t = σ_t × A_t(d,p,t) • A_t = (p - d) × t • σ_t = tensile strength of plate • Example: P_t = 61,875 lbf

## Slide 20
Hole Effect on Tearing Strength
Steam School Notes | 12 Riveted Joints
Rivet hole reduces plate tearing strength
• Hole diameter 0.750 in reduces capacity to 61,875 lbf • No hole capacity: 78,750 lbf • Reduction due entirely to removed metal
Larger rivet diameter increases shear strength but removes more metal, reducing tearing strength.

## Slide 21
Shearing of Rivet
Steam School Notes | 12 Riveted Joints
Rivet transfers load and may fail by shear
• Rivet cross-sectional area resists shear • A_s = π(d/2)² • Load-carrying capacity in single shear

## Slide 22
Single Shear
Steam School Notes | 12 Riveted Joints
Load cuts rivet along one shear plane
• Lap joint or single-cover butt joint configuration • One shear plane must fail • P_s = σ_r × π × (d/2)² • Example: P_s = 19,438.6 lbf with d = 0.750 in

## Slide 23
Double Shear
Steam School Notes | 12 Riveted Joints
Two shear planes must fail before rivet severs
• Double-cover butt joint configuration • Two shear planes resist failure • P_d ≈ 2 × P_s • NBIC uses factor of 2.0 for evaluation
Some authorities use 1.75 factor to account for unequal loading of two shear planes.

## Slide 24
Crushing of Rivet
Steam School Notes | 12 Riveted Joints
Excessive bearing pressure compresses rivet material
• Rivet bears against hole wall under load • Compression differs from shearing failure • Contact area resists crushing: A_c = d × t

## Slide 25
Crushing Strength Calculation
Steam School Notes | 12 Riveted Joints
Crushing force equals bearing stress times contact area
• P_c = σ_c × d × t • σ_c = bearing stress of rivet material • d = rivet diameter, t = plate thickness • Example: P_c = 26,718.8 lbf
Increasing rivet diameter or plate thickness increases crushing resistance.

## Slide 26
Tearing of Plate Margin
Steam School Notes | 12 Riveted Joints
Rivet too close to edge tears out margin material
• Metal between hole and edge resists failure • Two sections: one on each side of hole • Total resisting area: A_ms = 2 × m × t • m = margin (edge distance)

## Slide 27
Plate Margin Failure Load
Steam School Notes | 12 Riveted Joints
Tearing force depends on margin and plate thickness
• P_ms = 2 × m × t × σ_t • σ_t = tensile strength of plate material • Example: P_ms = 90,000 lbf with m = 2 in • Rivets must locate far enough from plate edge

## Slide 28
Summary of Failure Modes
Steam School Notes | 12 Riveted Joints
Four failure modes determine joint strength
• P_t (tearing): 61,875 lbf • P_s (shearing): 19,438.6 lbf • P_c (crushing): 26,718.8 lbf • P_ms (margin tear): 90,000 lbf
Weakest mode (shearing at 19,438.6 lbf) governs joint strength.

## Slide 29
Joint Strength Analysis
Steam School Notes | 12 Riveted Joints
Safe load determined by weakest failure mode
• Calculate load for each failure mode • Safe load = smallest calculated load • Well-designed joint proportions modes equally • Standard sizes limit optimization

## Slide 30
Design Optimization Limits
Steam School Notes | 12 Riveted Joints
Standard sizes constrain joint proportioning
• Plate thicknesses available in standard sizes • Rivet diameters in increments of 1/16 inch • Rivet spacing limited by measurement practicality • Theoretical optimum often unachievable

## Slide 31
Design Verification Process
Steam School Notes | 12 Riveted Joints
Designer selects standard dimensions and verifies safety
• Select dimensions from available materials • Calculate joint strength for each failure mode • Verify joint is safe for service • Design is compromise between efficiency, practicality, economy

## Slide 32
Analysis Assumptions
Steam School Notes | 12 Riveted Joints
Equations based on simplifying assumptions
• Real joints do not satisfy assumptions exactly • Loads not perfectly distributed • Rivets may bend slightly • Stress concentrations exist around holes • Friction between plates carries part of load
Assumptions provide sufficiently accurate calculations for practical boiler design.

## Slide 33
Joint Efficiency
Steam School Notes | 12 Riveted Joints
Ratio of riveted joint strength to solid plate strength
• Solid plate stronger than riveted plate • Rivet holes remove metal • Efficiency = weakest mode load / solid plate load • Ideally all modes have equal strength

## Slide 34
Calculating Joint Efficiency
Steam School Notes | 12 Riveted Joints
Efficiency calculation uses minimum failure load
• E = min(P_t, P_s, P_c, P_ms) / P_l • P_l = solid plate strength = p × t × σ_t • Standard sizes prevent equal mode strengths • Use minimum (weakest) mode in formula

## Slide 35
Efficiency on Blueprints
Steam School Notes | 12 Riveted Joints
Joint efficiencies specified on boiler blueprints
• Usually stated on boiler blueprints • Typical efficiencies used when drawings unavailable • Shell plate between seams has full strength • Seams do not
Joint efficiency used when determining maximum allowable working pressure of riveted boilers.