## Slide 1
Energy Required for Steam Engine Startup
Steam School Notes | 14 Properties of Water and Steam
800,000 kJ powers engine from cold to working pressure
• Equivalent to 7 days powering a house • 150 hours running a 1.5 kW heater • 3 hours running a 100 horsepower engine • 150–200 miles driving a car • Lifting 1000 kg to 80 km height
A working traction boiler is a large energy reservoir before producing useful work.

## Slide 2
Energy Context: Battery and Fuel Comparison
Steam School Notes | 14 Properties of Water and Steam
800,000 kJ equals energy in 3–4 modern EV battery packs
• 222 kWh requires 550–740 litres of lithium-ion battery volume • Modern Toyota Camry trunk holds 428 litres • Level-2 charger takes 20–30 hours continuous charging • Equivalent to nearly 500,000 wooden matches (wood only)

## Slide 3
Eight Core Quantities in Steam Work
Steam School Notes | 14 Properties of Water and Steam
Steam calculations rely on mass, volume, temperature, pressure, energy, power, and heat
• Mass — amount of water or steam • Volume — water space, steam space, tender, wagon • Temperature — sensible heat, saturation temperature • Pressure — boiler pressure, steam-table lookup • Energy — heat added or removed • Power — rate of heat transfer • Specific heat & latent heat — energy storage in water • Specific volume — why steam masses fill large spaces
These eight quantities form the backbone of all boiler physics.

## Slide 4
Unit Systems: Historical vs. Analytical
Steam School Notes | 14 Properties of Water and Steam
Historical dimensions in imperial units; analysis in SI units
• Machines conceived in inches and pounds • Physics most clearly expressed in kilograms, metres, seconds • Historical boiler pressures reported as gauge (PSIG) • Gauge pressure referenced to local atmospheric pressure • Thermodynamic analysis converts gauge to absolute pressure

## Slide 5
Mass Units
Steam School Notes | 14 Properties of Water and Steam
SI uses kilogram; Imperial uses pound-mass
• SI: kilogram (kg) • Imperial: pound-mass (lb)

## Slide 6
Volume Units
Steam School Notes | 14 Properties of Water and Steam
SI uses litre and cubic metre; Imperial uses gallon and cubic foot
• SI: liter (L), cubic meter (m³) • Imperial: gallon (US gal), cubic foot (ft³)
Boiler capacity and steam-space volume always given in these units.

## Slide 7
Temperature Units and Conversion
Steam School Notes | 14 Properties of Water and Steam
Absolute scales required for thermodynamic calculations
• SI: degrees Celsius (°C), kelvin (K) • Imperial: degrees Fahrenheit (°F), Rankine (°R) • T(Kelvin) = T(Celsius) + 273 • T(Rankine) = T(Fahrenheit) + 459.670 • ΔT uses K or °R; °C and °F cannot be mixed directly

## Slide 8
Pressure Units and Conversions
Steam School Notes | 14 Properties of Water and Steam
Steam tables use absolute pressure; boiler gauges show gauge pressure
• SI: kilopascal (kPa), bar • Imperial: pounds per square inch (psi) • 1 kPa = 100 bar • 1 bar = 14.504 psi
Steam tables use absolute pressure relative to vacuum; boiler gauges show gauge pressure relative to atmosphere.

## Slide 9
Energy Units
Steam School Notes | 14 Properties of Water and Steam
SI uses joule; Imperial uses British thermal unit
• SI: joule (J), kilojoule (kJ), megajoule (MJ) • F = M·A yields 1 N = 1 kg·m/s² • 1 J = 1 m·N = 1 kg·m²/s² • Imperial: British thermal unit (BTU) • 1 BTU = 1055.056 J
1 joule lifts a small apple 100 cm, runs 1-watt device 1 second, or raises 1 gram water 0.239°C.

## Slide 10
Power Units
Steam School Notes | 14 Properties of Water and Steam
Power is the rate of energy transfer over time
• SI: watt (W), kilowatt (kW) • Imperial: BTU/h, boiler horsepower (BHP) • 1 BHP = 33,475 BTU/h = 9.81 kW
Energy is capacity to do work; power is the rate at which work is done.

## Slide 11
Specific Heat
Steam School Notes | 14 Properties of Water and Steam
Specific heat quantifies energy required to raise temperature of unit mass
• SI: kJ/(kg·K) • Imperial: BTU/(lb·°F) • Used in all heat calculations: Q = m·c·Δt • m is mass, c is coefficient by material type, Δt is temperature change

## Slide 12
Latent Heat
Steam School Notes | 14 Properties of Water and Steam
Latent heat is energy for phase change without temperature change
• Latent heat of fusion: solid to liquid phase change • Latent heat of vaporization: liquid to vapor phase change • SI: kJ/kg • Imperial: BTU/lb

## Slide 13
Specific Volume
Steam School Notes | 14 Properties of Water and Steam
Specific volume explains why small steam masses occupy large volumes
• SI: m³/kg • Imperial: ft³/lb • Inverse of density • Preferred in thermodynamics for cleaner energy and state equations per unit mass

## Slide 14
Steam Tables Overview
Steam School Notes | 14 Properties of Water and Steam
Steam tables compile experimental thermodynamic properties at different conditions
• Saturation — boundary between liquid water and steam • Phase — whether substance is liquid, vapor, or mixture • Property sets — values needed for energy and volume calculations
Steam tables are compilations of experimentally determined data, not simple formulas.

## Slide 15
Selecting the Correct Steam Table
Steam School Notes | 14 Properties of Water and Steam
Three table types serve different thermodynamic regimes
• Saturated table: use when water is boiling (T and P linked) • Superheated table: use when steam is hotter than saturation • Compressed water table: rarely needed in boiler work

## Slide 16
Converting Gauge Pressure to Absolute
Steam School Notes | 14 Properties of Water and Steam
Thermodynamic analysis requires absolute pressure relative to vacuum
• P(absolute) = P(gauge) + 101.300 kPa • Or add 14.7 psi in Imperial units

## Slide 17
Reading the Saturated Table
Steam School Notes | 14 Properties of Water and Steam
Extract properties at saturation from pressure or temperature row
• Find row for your pressure or temperature • Read vf, vg, hf, hfg, hg where subscripts f and g stand for fluid and gas • Latent heat is hfg = hg – hf

## Slide 18
Wet Steam Quality
Steam School Notes | 14 Properties of Water and Steam
Quality factor x represents fraction of vapor in two-phase mixture
• h = hf + x·hfg • v = vf + x·(vg – vf) • x ranges from 0 (dry liquid) to 1 (dry vapor) • Used only in two-phase region where liquid and vapor coexist at saturation

## Slide 19
Reading the Superheated Table
Steam School Notes | 14 Properties of Water and Steam
Extract properties of steam hotter than saturation temperature
• Start with pressure section • Move across to temperature column • Read h, u, v for superheated vapor

## Slide 20
Common Steam Table Mistakes
Steam School Notes | 14 Properties of Water and Steam
Errors in table use lead to incorrect thermodynamic calculations
• Using gauge pressure instead of absolute • Mixing SI and Imperial units • Confusing hf (liquid) with hg (vapor) • Assuming latent heat is constant • Misreading vg (steam volume) by orders of magnitude
Errors in table use compromise all downstream calculations.

## Slide 21
Boiler Warmup: Three Physical Stages
Steam School Notes | 14 Properties of Water and Steam
Boiler transitions through heating, boiling, and pressurization regimes
• Stage 1: Sensible heating from ambient to 100°C at 1 bar • Stage 2: Boiling at constant temperature to fill steam space • Stage 3: Heating to saturation temperature at final pressure
Each stage has distinct energy requirements and physical meaning.

## Slide 22
Boiler Warmup: Piecewise Function
Steam School Notes | 14 Properties of Water and Steam
Boiler transitions through heating, boiling, and pressurization regimes
Each stage has distinct energy requirements and physical meaning.

## Slide 23
Stage 1: Warming Water and Steel to Boiling
Steam School Notes | 14 Properties of Water and Steam
All heat raises temperature; no steam produced; pressure stays at 1 bar
• Energy range: 0 ≤ q < q₁ • q₁ = C(warm) × (100 – T₀) • C(warm) = mw·cw + ms·cs • No phase change; boiler is thermally sluggish
Heat is applied to a large thermal mass with no pressure rise.

## Slide 24
Stage 2: Boiling at Constant Temperature and Pressure
Steam School Notes | 14 Properties of Water and Steam
Temperature fixed at 100°C while boiling fills steam space at 1 bar
• Energy range: q₁ ≤ q < q₂ • Δq = (Vs / vv(1)) × Hv(1) • q₂ = q₁ + Δq • Temperature stops rising; all heat goes into latent heat
Temperature stays at 100°C while enough 1-bar steam fills the steam space.

## Slide 25
Stage 3: Pressurization to Operating Pressure
Steam School Notes | 14 Properties of Water and Steam
Heat raises temperature and generates denser steam to reach final pressure
• Energy range: q₂ ≤ q < q₃ • Sensible heating: C(warm) × [Tsat(Pset) – 100] • Steam generation: (Vs / vv(Pset)) × Hv(Pset) • Pressure rises only after steam space is full
Pressure rises only after the steam space is full.

## Slide 26
Final State: Boiler at Operating Pressure
Steam School Notes | 14 Properties of Water and Steam
Boiler ready for work at saturation temperature and pressure
• Energy range: q ≥ q₃ • Full of saturated steam at Pset • Water and steel at Tsat(Pset) • Ready for work; temperature fixed at saturation

## Slide 27
Saturation Curve Relationship
Steam School Notes | 14 Properties of Water and Steam
Saturation temperature is monotonic function of pressure
• At 1 bar: water boils at 100°C • At 2 bar: approximately 120°C • At 10 bar: approximately 180°C • Saturation temperature increases monotonically with pressure
If pressure increases on boiling water, the boiling point increases.

## Slide 28
Empirical Saturation Temperature Formula
Steam School Notes | 14 Properties of Water and Steam
Simple approximation captures saturation curve without full steam tables
• Tsat(P) = 100 + 35.4·ln(P) • Constant 100 anchors curve at 1 bar • Logarithmic term gives correct shape: slow rise at low pressure, faster at moderate, flattening at high • Good for conceptual modeling, plotting, energy budgets
Logarithmic form mimics saturation curve without needing full steam tables.

## Slide 29
Latent Heat of Vaporization
Steam School Notes | 14 Properties of Water and Steam
Energy needed to convert saturated water to steam without temperature rise
• Hv(P) = 2257 – 2.3·(Tsat(P) – 100) • At 1 bar: approximately 2257 kJ/kg • Decreases with increasing pressure • At higher pressure, liquid becomes more like vapor; energy gap shrinks
Latent heat gets smaller at higher pressure; at critical point it becomes zero.

## Slide 30
Specific Volume of Saturated Steam
Steam School Notes | 14 Properties of Water and Steam
Steam density decreases with pressure; increases with temperature
• vv(P) = 0.004·(Tsat(P) + 273) / P • Low pressure: steam is fluffy; large volume per kg • High pressure: steam is denser; smaller volume per kg • Same steam space contains more mass at higher pressure
Steam volume per unit mass follows ideal gas law: v ∝ T/P.

## Slide 31
Energy to Fill Steam Space at 1 Bar
Steam School Notes | 14 Properties of Water and Steam
Δq = mass × latent heat; mass determined by steam space volume
• Δq = (Vs / vv(1)) × Hv(1) • Vs / vv(1) = kilograms of steam to fill space at 1 bar • Hv(1) ≈ 2257 kJ/kg at 1 bar • At 1 bar, steam space volume is large; required mass is small
Small steam mass requires small latent-heat energy; transition to pressurization is rapid.

## Slide 32
Rapid Transition to Pressurization
Steam School Notes | 14 Properties of Water and Steam
Boiler dwells briefly at 100°C before pressure begins rising
• Steel mass dominates thermal capacity during warm-up • Once steel reaches 100°C, sensible heating ceases • Steam space volume is small; steam mass required is minimal • Latent heat for this small mass is correspondingly small
System transitions rapidly from atmospheric boiling to pressurization.

## Slide 33
Worked Example: Heating a Kettle
Steam School Notes | 14 Properties of Water and Steam
Kettle physics mirrors boiler physics at household scale
• Mass: 2.0 kg water • Initial temperature: 20°C • Final temperature: 100°C • Specific heat: 4.18 kJ/(kg·K) • Heater power: 2.0 kW

## Slide 34
Kettle Example: Energy Calculation
Steam School Notes | 14 Properties of Water and Steam
Sensible heat equals mass times specific heat times temperature rise
• Q = m·c·ΔT • Q = 2.0 kg × 4.18 kJ/(kg·K) × 80 K • Q ≈ 668.8 kJ ≈ 670 kJ • Same approach used for boiler calculations

## Slide 35
Kettle Example: Time Calculation
Steam School Notes | 14 Properties of Water and Steam
Time equals energy divided by power; result independent of scale
• t = Q / Qdot = 670 kJ / 2.0 kJ/s = 335 s • 335 s ≈ 5.5–6 minutes • No losses assumed • With losses, time increases
A 2.0 kW kettle heats 2.0 kg from 20°C to 100°C in about 5.5–6 minutes.

## Slide 36
Kettle-to-Boiler Scaling
Steam School Notes | 14 Properties of Water and Steam
Same structure applies at all scales; only mass and power differ
• Compute Q = m·c·ΔT for the water mass • Divide by net heat rate to get time • At boiler scale: m is hundreds of kg; power from fuel and efficiency
Boiler warmup uses identical reasoning at different mass and power scales.

## Slide 37
Pressure Rise in Sealed Boiler
Steam School Notes | 14 Properties of Water and Steam
Temperature and pressure locked by saturation curve; sensible heat dominates
• Q(pressurize) = m·c·[Tsat(Ptarget) – Tsat(initial)] • Entire water mass must be heated along saturation curve • Latent heat contribution small; steam space mass is minimal • Energy requirement large despite small temperature rise

## Slide 38
Effect of Firing Rate on Warmup Time
Steam School Notes | 14 Properties of Water and Steam
Higher firing rate reduces time to reach pressure despite constant energy need
• Energy requirement is thermodynamic; same regardless of rate • Time = Energy / Power • Higher heat transfer rate decreases time proportionally • Practical firing rates limited by thermal shock and control

## Slide 39
Traction Boiler Geometry: Barrel
Steam School Notes | 14 Properties of Water and Steam
Barrel is primary pressure vessel; cylindrical geometry dominates volume
• Typical 25 BHP: 30 inch diameter, 96 inch length • Volume: V(cyl) = π(D/2)²·L • Barrel volume approximately 39 ft³ • Forms core of heat transfer surface

## Slide 40
Boiler Water and Steam Spaces
Steam School Notes | 14 Properties of Water and Steam
Total boiler volume divided into water and steam spaces by water level
• Total boiler volume: approximately 50 ft³ (1.42 m³) • Steam space volume: approximately 11.8 ft³ (0.335 m³) • Water space: approximately 38.2 ft³ (1.08 m³) • Water capacity: approximately 238 gallons
Steam space is roughly 20% of total; water fills remaining volume.

## Slide 41
Boiler Steel Mass
Steam School Notes | 14 Properties of Water and Steam
Steel thermal capacity adds to water mass in warmup calculation
• Typical 25 BHP boiler steel: approximately 3,556 lb (1,613 kg) • Specific heat of steel: 0.49 kJ/(kg·K) • Significant thermal mass; slows warmup substantially • Must be included in sensible-heat calculations

## Slide 42
Phase 1 Warmup: Cold to First Boil
Steam School Notes | 14 Properties of Water and Steam
Heating 1,082 kg water and 1,613 kg steel from 20°C to 100°C
• Temperature rise: 80 K (80°C = 144°F) • Water sensible heat: 362 MJ • Steel sensible heat: 63 MJ • Total required: 425 MJ • Observed time: approximately 2 hours
Net heat rate required: 59 kW reaching water and boiler steel.

## Slide 43
Wood Firing to Achieve Phase 1 Warmup
Steam School Notes | 14 Properties of Water and Steam
Realistic fuel consumption matches observed warmup time
• Wood lower heating value: 8–12 MJ/kg • Boiler efficiency on wood: 30–45% • Using 10 MJ/kg, 35% efficiency • Fuel required: 121 kg (267 lb) wood • Burning rate: approximately 150 lb/hour
Phase 1 consumes about 300 lb wood before boiling begins.

## Slide 44
Phase 2: Raising Pressure from 0 to 100 psi
Steam School Notes | 14 Properties of Water and Steam
Heating from 100°C to 170°C while generating steam at higher pressure
• Temperature rise: 70 K (70°C = 126°F) • 100 psi ≈ 8 bar ≈ 170°C saturation • Water sensible heat: 333 MJ • Steel sensible heat: 58 MJ • Steam generation: 3 MJ • Total required: 394 MJ
Energy requirement in Phase 2 similar to Phase 1 despite smaller temperature rise.

## Slide 45
Latent Heat in Sealed-Boiler Pressurization
Steam School Notes | 14 Properties of Water and Steam
Latent heat dominates pressure rise despite small latent-heat component
• Latent heat generates steam that fills fixed steam space • Huge volume ratio vg/vf drives pressure increase • Small steam mass at high pressure fills same space as large mass at low pressure • Therefore: pressure responds nonlinearly to small sensible temperature increases
Latent heat requirement is relatively small; sensible heat of water dominates.

## Slide 46
Practical Phase 2 Warmup Time
Steam School Notes | 14 Properties of Water and Steam
0 to 100 psi typically takes 1.5–2 hours at moderate firing rate
• Energy requirement: 394 MJ (similar to Phase 1) • Energy per unit time: adjusted for firing rate • Steam-induced draft assists pressure rise after 5–10 psi • Operator experience affects actual time
Phase 2 duration similar to Phase 1 because sensible heat dominates.

## Slide 47
Steam Velocity and Injector Operation
Steam School Notes | 14 Properties of Water and Steam
High steam velocity at boiler pressure powers injector entrainment
• Boiler pressure steam: huge specific volume • Speed of sound in steam: 450–500 m/s • Nozzle velocities: 300–500 m/s • Water through nozzle: only 40–50 m/s at same pressure
Same physics making pressure rise quickly makes steam extremely fast.

## Slide 48
Injector Principle
Steam School Notes | 14 Properties of Water and Steam
High-velocity steam jet entrains water, condenses, drives mixture into boiler
• Velocity difference between steam and water is foundation of injector operation • Steam jet speed: 300–500 m/s • Water stream speed: 40–50 m/s • Velocity difference enables water entrainment and compression
This velocity difference is direct consequence of boiler thermodynamics.