## Slide 1
Chapter Overview: Isolation Valves
Steam School Notes | Chapter 4 Isolation Valves
Introduction and importance of isolation valves in boiler operation
Checking valve positions is one of the first tasks when approaching a boiler for operation.
Valve positions can change, especially in museum settings with frequent handling.
Isolation valves are shut-off valves in the boiler's plumbing system.

## Slide 2
Purpose of Isolation Valves
Steam School Notes | Chapter 4 Isolation Valves
Isolation Valves - Purpose
Enable removal of a fitting, line, or accessory from service without dropping boiler pressure or draining the system.
Allow isolation of components for proving, cleaning, repair, or replacement while the rest of the boiler remains pressurized and in water.
Installed on any line that must occasionally be serviced: steam, water, or blowdown lines.

## Slide 3
Requirements for Isolation Valves
Steam School Notes | Chapter 4 Isolation Valves
Isolation Valves - Valve Type Requirements
Withstand full boiler pressure
Withstand steam temperature
Seal positively when closed
Be fully open in normal operation
Be located as close to the boiler shell as practical
If a valve cannot meet these requirements, it is not suitable for isolation duty on a boiler.

## Slide 4
Location of Isolation Valves on the Boiler
Steam School Notes | Chapter 4 Isolation Valves
Isolation Valves - Installation Location
Always installed as close to the boiler shell as practical to minimize exposed pipe or fittings when closed.
Marks the boundary between 'boiler proper' and 'serviceable plumbing.'
Isolation valves on a traction engine include:
Steam and water isolation valves for the gauge glass
Turret isolation valve feeding the accessory manifold
Injector steam and water isolation valves
Blower isolation valve
Blowdown valve at the lowest point of the boiler

## Slide 5
Isolation Valve Position During Operation
Steam School Notes | Chapter 4 Isolation Valves
Isolation Valves - Operating Position
During normal steaming, all isolation valves serving operating equipment must be fully open.
Full opening ensures each device sees true boiler pressure and unrestricted flow.
Isolation valves are closed only when isolating a component for maintenance, proving, or safety.
Gauge glass with either isolation valve shut will lie
Injector with steam or water valve partly closed will not pick up
Blower or turret line with isolation valve shut will appear dead

## Slide 6
Finding Isolation Valves on a Boiler
Steam School Notes | Chapter 4 Isolation Valves
Isolation Valves - Location and Identification
General rule: if a fixture is connected to the steam or water space, an isolation valve should be present at the closest point to the boiler.
Isolation valve locations by system:
Injectors
  At the feedwater entry
  At the steam supply
Main steam line
  At the dome
Water column
  On the steam side
  On the water side
Whistle
Gauge
Blower
  On some engines, the blower is fed from the injector steam supply and is isolated when the injector is isolated
Isolation valve locations by system:
Injectors
  At the feedwater entry
  At the steam supply
Main steam line
  At the dome
Water column
  On the steam side
  On the water side
Whistle
Gauge
Blower
  On some engines, the blower is fed from the injector steam supply and is isolated when the injector is isolated